## Slide 1: deMorgans Laws, logical expressions and Truth Tables
AP Computer Science

## Slide 2
Boolean Addition and Multiplication
The OR operation is often called Boolean addition. Variables that are ORed together form a sum term.
The AND operation is often called Boolean multiplication. Variables that are ANDed together form a product term.
Example #1
The expression (A+B+C)(D+E) is the product of two sum terms.
Example #2
The expression AB + CD + AD is the sum of three product terms.

## Slide 3
Commutative Laws
The order in which variables are ORed makes no difference.
The commutative law of addition states that
A + B = B + A
The order in which variables are ANDed makes no difference.
The commutative law of multiplication states that
AB = BA
Notes: Show what this means in terms of gates.

## Slide 4
Associative Laws
When ORing more than two variables, the result is the same regardless of the grouping of the variables.
The associative law of addition states that
A + (B +C) = (A + B) + C
The associative law of multiplication states that
When ANDing more than two variables, the result is the same regardless of the grouping of the variables.
A(BC) = (AB)C
Notes: Show what this means in terms of gates.

## Slide 5
Distributive Law
The distributive law is the factoring law. A common variable can be factored from an expression just as in ordinary algebra. That is
AB + AC = A(B+ C)

## Slide 6
Rules of Boolean Algebra
3. A + 0 = A
4. A + 1 = 1
1. A . 0 = 0
2. A . 1 = A
6. A + A = A
5. A . A = A
8. A + A = 1
7. A . A = 0
9. A = A
=
10. A + AB = A + B
Notes: -Discuss Rules 1 to 9 in terms of truth tables of basic gates.
-Rules 10 can be derived from the others; it’s a shortcut rule that may be useful.

## Slide 7: Augustus DeMorgan
My name is Augustus DeMorgan. I’m an Englishman born in India in 1806. I was instrumental in the advancement of mathematics and am best known for the logic theorems that bear my name.
P.S. George Boolean gets WAY too much credit. He has more theorems, but mine are WAY Cooler! Take a look at them, OMG, they are the bomb.
Notes: A little history…
http://www.math.utep.edu/Faculty/mleung/probabilityandstatistics/chronology.htm

## Slide 8
DeMorgan’s Theorems
The complement of a product of variables is equal to the sum of the complemented variables.
DeMorgan’s 1st Theorem
AB = A + B
Notes: -Here it’s written for 2 terms, but it applies to any number of terms: e.g., (ABC)’ = A’ + B’ + C’

## Slide 9
DeMorgan’s Theorems
DeMorgan’s 2nd Theorem
The complement of a sum of variables is equal to the product of the complemented variables.
A + B = A . B
Notes: -Here it’s written for 2 terms, but it applies to any number of terms: e.g., (A+B+C)’ = A’B’C’

## Slide 10
Apply DeMorgan’s theorem to remove the overbar covering both terms from the
expression X = C + D.
DeMorgan’s Theorem
Example
Solution
Notes: -Another example: ((A+B)C)’ = A’B’ + C’
-Another example: (AB’ + C’D)’ = (A’+B)(C+D’)

## Slide 11: NAND equals “Negative OR”

## Slide 12: NOR equals “Negative AND”

## Slide 13
Simplifying NAND Circuits
Recall that, according to Demorgan’s theorem, the following two representations of a NAND gate are equivalent:

## Slide 14
Sum-of-Products form
A Boolean expression is in sum-of-products form (SOP) when it’s written as the sum of one or more products. In SOP form, an overbar cannot extend over more than one variable.
Examples of expressions in SOP form:
Product-of-sums form (POS), in which two or more sum terms are multiplied, as in the following examples:
SOP form is more useful than POS form.
A B C + A B A B C + C D AB +AC + D
(A + B)(A + C) (A + B + C)(B + D) (A + B)(B+C)D
Notes: -The K-map technique requires you first to put your expression in SOP form.

## Slide 15: Truth Table & Logic Expressions
This presentation will demonstrate how to…
Properly construct a truth table.
Write a Sum-Of-Products (SOP) logic expression from a truth table.
Create a truth table given a SOP logic expression.
Create a truth table from a set of design specifications (i.e., word problem).
X | Y | OUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
EQUALS
EQUALS
Design
Specifications
Truth Table
Logic
Expression
Notes: Introductory Slide / Overview of Presentation

## Slide 16: Constructing A Truth Table
A truth table shows how a logic design’s output respond to ALL combinations of possible inputs.
A logic design with N inputs will have 2N input combinations.
The input are listed in binary order (i.e., counting order) in the columns to the left.
The output(s) are listed in the column(s) to the right. (Note some logic circuits can have more than one output.)

## Slide 17: Constructing A Truth Table
X | Y | Z | F1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Inputs
Output
Input Combinations
  3 – Inputs
  8 – Combinations
  (8 = 23)
Note the binary counting
order of the inputs :
0002 = 010
0012 = 110
0102 = 210
0112 = 310
1002 = 410
1012 = 510
1102 = 610
1112 = 710
Outputs for Each Input Combination
Notes: Example of a three input / one output truth table

## Slide 18: MinTerms and Maxterms

## Slide 19: Minterms Examples

## Slide 21: Create Two Logical Expressions for the truth tables
A | B | F2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X | Y | Z | F3
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
R | S | T | U | F4
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
3 Inputs
23 = 8 Combinations
4 Inputs
24 = 16 Combinations
2 Inputs
22 = 4 Combinations
Notes: Format for a 2, 3, & 4 variable true table

## Slide 22
SOP and POS forms
Many Boolean expressions are in neither SOP form nor POS form.
Example 1: A(B + C + BC) + (AB + AB)C
Example 2: AB + C(AD + BD)
But every expression can be converted to SOP form by applying some or all of the following: DeMorgan’s theorems, the distributive law, and the commutative law.
Notes: -Convert the slide’s two examples to SOP form: A’B’C + A’BC + ABC + AB’C and AB + A’CD + BCD’.
-Set up these 2 examples to both sides of the screen.

## Slide 23
REVIEW: Writing the SOP Expression for any Truth Table
Given the truth table for a expression, it’s easy to write an SOP-form expression for that expression.
Step 1. For each of the truth table’s rows with a 1 in the output column, list the corresponding product term of the input variables.
Step 2. Add all of the product terms from Step 1.
See example on next slide…

## Slide 24: Sample AP Computer Science Question I

## Slide 25: Sample ap computer science Question II

## Slide 26: Summary
Commutative Law
Associative Law
Distributive Law
Consensus Theorem
Boolean & DeMorgan’s Theorems
DeMorgan’s
Notes: Updates of the Boolean Theorems with the addition of DeMorgan’s